## Slide 1: ATLYS AC ‘97 Codec, RAM, & LCD Interface
Materials for Final Project

## Slide 2: Source Materials
Final project source files are available on Canvas
Datasheets, etc also on Canvas
  Check the 'Modules' section.

## Slide 3: AC ‘97 Overview

## Slide 4: Audio Interface Overview
AD1981A Codec
Up to 48-kHz sampling, 16-bit audio
  Downsampled to 8
AC97 FPGA Interfaces
  Audio Bit Clock
  Audio Serial Data In/Out
  Audio Sync
  Audio Reset

## Slide 5: ATLYS AC’97 Interface

## Slide 6: Overview (Cont’d)
All commands and data communicated through serial interconnects (In/Out)
Requires clock input (Bit Clock)
  Used for control/processing
Uses independent frame synchronization signal (Audio Sync)
  Regulates bitrate for capture and playback sampling

## Slide 7: Basic Setup
Verilog Module
HW on FPGA

## Slide 8: AD1981A Quick Details
Inputs 12.288 MHz Bit Clock
Uses SDATA_IN/OUT to communicate with controller
  Timed with bit clock, specified in data sheet
Uses 48 kHz SYNC signal
  Controls sample rate for recording and playback
Contains various control inputs/outputs for advanced codec control
  Functions are controlled by the ATLYS, cannot be modified
  Includes mode select, variable bitrate, audio channels
  Handles power management

## Slide 9: Verilog Codec Interface – ac97audio.v
Handles timing, control interface, and data transfer
Interface operates off of system clock
Outputs 8-bit audio from microphone jack
  Samples at 48 kHz
Inputs 8-bit audio for playback over headphone jack
Inputs 5-bit volume value
  Should be controlled by user interface

## Slide 10: Verilog Codec Interface – ac97audio.v (Cont’d)
Interfaces directly with ac97 control and data pins on board
Handles codec reset
Handles codec initialization and audio buffering
Fixed bitrate
Requires ac97commands.v and ac97.v
Simplifies controller operation
You should read through the code to understand the functionality

## Slide 11: Questions?

## Slide 12: RAM Interface
Provides access to 1 Gbit of onboard DDR2 RAM.
Requires modified clocking
  Design will operate at 37.5 MHz
Interface consists of IP Core and Wrapper.
  Provides 8-bit data interface
  26-bit addressing
Single-Step Write Operation
  Write `data_in` to `address`
Two-Step Read Operation
  Request data from `address`
  Wait for ready
  Get data & acknowledge

## Slide 13: Installing
Copy 'ram_interface_wrapper.v' to your project root
Extract the contents of IPCore.zip to the `ipcore_dir` folder in your project root.
  If it does not exist, create it.
Add to ISE Project
  From ISE, select 'Project->Add Source' (NOT copy)
  Select `ram_interface_wrapper.v` and `ipcore_dir/ram_interface.xise`

## Slide 14: Using the RAM Interface
General
  reset: [input] synchronous reset
  clk: [input] 100MHz clock
  clkout: [output] 37.5 MHz System Clock
  sys_clk: [input] 37.5 MHz System Clock (Yes, you have to route this yourself)
  rdy: [output] '1' signals that the interface is ready for use.
Writing
  Single-operation write
  When `write_enable` goes high, the value of `data_in` is written to loc `address`
Reading
  Two-operation write
  When `read_request` goes high, the system queues a READ from loc `address`
  When read is ready, `rd_data_pres` goes high, & data is available at `data_out`
  When reading data, acknowledge with a `1` on `read_ack`

## Slide 15: Questions?

## Slide 16: LCD Overview
2-Line 16-Character display
Tianma TM162VBA6 Controller
  Equivalent to controller covered in provided info sheet (LCDmanual1.pdf) on Blackboard
Displays standard Character set
Onboard RAM to store characters
Controller accepts 8-bit data
  Sent in 4-bit or 8-bit mode

## Slide 17: Connecting to LCD
LCD Connection is achieved via PMOD connector.
Pins 1-4 connect to LCD_DATA[4:7]
Pins 7-9 connect to RS, RW, EN (in that order)
  Pin 10 not connected
PMOD pigtail connector
  Large connector goes DOT SIDE DOWN
  Small connectors go LETTER SIDE UP.
  Connector A goes to COMMAND pins.
  Connector B goes to lower half of DATA pins.
See ATLYS datasheet for pin information
  Page 21, for the lazy.

## Slide 18: LCD Hookup

## Slide 19: LCD Functionality
Only 4-bit data transfer available
  4-bit mode requires slightly more complex timing
  Timing details available in info sheet
Control Functionality
  Clear Display
  Return Cursor Home
  Entry Mode Set
  Display On/Off
  Cursor & Display Shift
  Function Set
  Set CG RAM Address
  Set DD RAM Address
  Read Busy Flag & Address
  Read/Write Data to CG or DD RAM
LCD Startup Sequence
Source: Digilent PMODCLP reference manual.

## Slide 20: LCD Characters

## Slide 21: Using the LCD Display
Step 1: Initialize the display
  After board power-up, send control signals, observing timing constraints
Step 2: Configure the display
  After initialization, set configuration details
    Entry Mode: Automatic or Manual address pointer incrementing
    Display On/Off:
      Turn on/off the display,
      Set cursor properties (Blink, visible, invisible)
    Clear Display

## Slide 22: Step 3 - ∞
Set starting address before writing data
Write data
  remember, 4-bit data transfer mode
Controller does NOT automatically move to next line, does NOT automatically scroll
  Must set line manually
  If more than 16 characters, can enable scroll mode

## Slide 23: Implementation & Use Details
Info sheet provided on Canvas
  Provides detailed usage instructions for LCD Interface
  Document is for Spartan 3, however it does apply to Virtex 5 controller
Tianma datasheet available online, if further details are required
Timing is extremely important for functionality
Sample Code for the LCD is available for Digilent
  Is for Spartan-3, 8-bit data. Must be modified.

## Slide 24: Questions?

## Slide 25: Design Considerations
Verilog AC ‘97 Interface only offers 1 sampling rate
Audio recording and playback must be continuous
LCD should always have the current message
Controls should always respond to inputs
“Reset” is an emergency-only button
  NOT part of functionality step
    Except for initialization
Synchronize Components
Proper Initialization of Components

## Slide 26: If You Get Stuck….
Follow these steps if you get stuck at some point
Determine where the problem is
Verify your Verilog code – Timings, I/O Ports, Pin Mappings, and Syntax
  Use Chipscope to verify timings and signals
  Use simulation to verify code functionality
Check your PicoBlaze Code
  Make sure your assembly is valid
  Check to make sure the registers/variables are correct
Check your timing and syntax again
Then, if you are still stuck, email the TA’s
  We can give suggestions, not solutions
  We cannot debug your code for you – use ChipScope, iSim and PBlazeIDE

## Slide 27: Good Luck!